2TON HYDRAULIC FOLDING

ENGINE CRANE

MAX.CAPACITY: 2TON

● INSTRUCTIONS ●

IMPORTANT: IT IS IMPORTANT THAT YOU READ AND UNDERSTAND THIS INSTRUCTION MANUAL BEFORE USING YOUR ENGINE CRANE. ALWAYS ENSURE ITS CORRECT USE, WHICH WILL HELP PREVENT DAMAGE AND INJURY.

OWNER/OPERATOR RESPONSIBILITY

- It is the owner/operator responsibility to properly use and maintain this equipment.

- The instructions and warning contained in this manual shall be read and understood by the owner/operator prior to operating this equipment.

- If an owner/operator does not understand English, the contents of this manual shall be explained in the owner/operators native language to assure that the owner/operator comprehends.

- The owner/operator shall retain this manual for future reference to important warnings, operating and maintenance instructions.

SPECIFICATION

Max. Capacity……………………………………………….….…..……………….…….…. 2Ton

Lifting capacity position 1………………………………….……..….………………….…... 2Ton

Lifting capacity position 2…………………………………………………..……………... 1½Ton

Lifting capacity position 3…………………………………..…………………….…….….... 1Ton

Lifting capacity position 4………………………………..………………………..……….. . ½Ton

Max. Lifting height: 2Ton ……………...……………………………………………..….. 1850MM

Max. Lifting height: ½Ton…..……………………………………………….………….… 2300MM

- WARNING

- WARNING: Do not overload. Overloading could cause damage or failure of the engine hoist.

- WARNING: Never use the hoist on an uneven floor surface as this could result in the hoist tipping over.

- WARNING: Always lock the legs and jib in position before lifting a load.

- WARNING: The nuts and bolts supplied with the hoist are all high strength and should not be substituted for inferior types.

- WARNING: Before each use ensure that all nuts and bolts are correctly fitted and tight.

- WARNING: Never exceed the safe working loads indicated on the jib.

- WARNING: FAILURE TO FOLLOW THESE INSTRUCTIONS COULD RESULT IN LOSS OF LOAD AND/OR PERSONAL INJURY OR DAMAGE TO PROPERTY.

INSPECTION

1. Visual inspection should be made before each use of the engine hoist.

2. Any engine hoist which appears to be damaged in any way is found to be badly worn, or operated abnormally must be removed from service.

3. If the engine hoist is accidentally subjected to an abnormal load or shock, it must be inspected by the manufacturer immediately.

4. It is recommended that an annual inspection of the engine hoist be made and that any defective parts, decals, or warning labels be replaced with manufacturer’s specified parts.

ASSEMBLY INSTRUCTIONS

- WARNING: During the assembly procedure, nuts and bolts should be hand tightened only. Once assembly is complete, nuts and bolts must be fully tightened.

- Attach two 3½” swivel castors (#9) and two 3” swivel castors (#10) to base frame using bolts (#21 and #22), nuts (#30) and lock washers (#31).

- Referring to the spare parts drawing, insert two legs (#4) into the base (#1) and lock the legs in place using four locking pins (#5). Secure these in place using four split- “R” pins (#7).

- Attach the main post (#3) to the base assembly (#1) using bolts (#19), nuts (#25) and flat washers (#26).

- Attach support straps (#6) to top of main post using bolt (#16), nut (#23) and flat washer (#24).

- Attach support straps (#6) to the base using bolts (#14), nuts (#23) and flat washers (#24).

- Now secure the boom (#2) to the main post (#3) using bolt (#15), nut (#23) and flat washer (#24).

- Connect bottom of ram unit (#11) to main post (#3) using bolt (#17), nut (#23) and flat washer (#24).

- While helper holds boom up. Connect top of hydraulic ram to boom using bolt (#18), nut (#23) and flat washer (#24).

- Slide boom extension (#13) into the main boom(#2),secure in one of the four positions using bolt (#19),nut (#25) and flat washer(#26).

- Tighten all nuts and bolts.

OPERATING INSTRUCTIONS

- WARNING: THIS LONG RAM JACK IS DESIGNED FOR LIFTING PURPOSES ONLY-NOT FOR SUPPORTING LOADS.

- WARNING: DO NOT LOAD BEYOND ITS RATED CAPACITY.

- WARNING: IMPORTANT: It is possible that air has got into the hydraulic system, causing poor lifting performance. Purge any air from the system by fully opening release valve (turn handle counterclockwise as shown), then while holding the boom down, operate pump handle rapidly several times.

TO RAISE LOAD

Close release valve by turning ram bleeder CLOCKWISE to a SNUG-TIGHT position. (DO NOT OVERTIGHTEN).

TO LOWER LOAD

Open release valve by turning handle COUNTERCLOCKWISE very slowly. The speed of lowering the load is controlled by how much you turn the hand.

- WARNING: Front legs must always be locked in down position before applying load and/or raising boom.

- WARNING: Boom must be in fully lowered position before raising legs. Legs must never be raised when crane is carrying load. Legs must be locked in place when raised.

PARTS DIAGRAM

PARTS LIST

| REF# | DESCRIPTION | QTY | REF# | DESCRIPTION | QTY |
| --- | --- | --- | --- | --- | --- |
| 1 | Base | 1 | 17 | Bolt M16x90 | 1 |
| 2 | Boom | 1 | 18 | Bolt M16x80 | 1 |
| 3 | Main Post | 1 | 19 | Bolt M14x100 | 3 |
| 4 | Leg | 2 | 20 | Bolt M12x80 | 1 |
| 5 | Lock Pin | 4 | 21 | Bolt M8x20 | 16 |
| 6 | Support Strap | 2 | 22 | Bolt M8x12 | 8 |
| 7 | Split ”R” Pin | 4 | 23 | Nut M16 | 6 |
| 8 | Chain & Hook Assembly | 1 | 24 | Flat WasherØ16 | 6 |
| 9 | 3½”Swivel Castor | 4 | 25 | Nut M14 | 3 |
| 10 | 3”Swivel Castor | 2 | 26 | Flat WasherØ14 | 3 |
| 11 | 8Ton Long Ram Jack | 1 | 27 | Nut M12 | 1 |
| 12 | Handle | 1 | 28 | Flat WasherØ12 | 1 |
| 13 | Boom Extension | 1 | 29 | Lock WasherØ12 | 1 |
| 14 | Bolt M16x100 | 2 | 30 | Nut M8 | 16 |
| 15 | Bolt M16x120 | 1 | 31 | Lock WasherØ8 | 24 |
| 16 | Bolt M16x110 | 1 |  |  |  |